## Slide 1: An optimization algorithm for Dial a Ride problems in the context of intermodal route planning
Research Project Defense
Supervisors:
Prof. Jakob Puchinger
Prof. Asmaa Ghaffari
Presented by Ayman MAHMOUD
Master 1 – Ingénierie des systèmes complexes
CentraleSupélec

## Slide 2: Overview:
Introduction
Key Figures & History
Motivation
Hypothesis
Methodology in Research
State of the art
Problem Definition
Results
Observations & Conclusion

## Slide 3: Introduction:
Questions raised:
  What are the research directions in mobility optimization?
  What is the relationship between shared mobility and public transport in research?
  Is there really a gap between shared mobility and public transport systems?
Importance:
  The increasing transportation demand in Europe. +42%
  The increase of public transport, network to serve a larger population.
  Suburban underserved areas.
  There is a clear aim in the EU to make the multimodal passenger transport as seamless as possible.
  If successfully implemented intermodal passenger transport will give more options to the traveler.
Objectives:
  Understand transportation science and modeling of passenger transport systems.
  Establish a framework that connects shared mobility with classical public transport.

## Slide 4: Key figures & history:
In the region of Ile de France there's 836km of accessible roads where 25% experience congestion in the peak hour.
15–20% of total GHG in the EU and the US are caused by ground transportation.
Congestion increase 15-20% between 2008 and 2018.
Operating companies with a transport feeder model.
The first ride-sharing as in car-sharing program was established in 1948 in Zurich.
Not an attractive solution during this period.

## Slide 5: A point of critique:
Ride-sharing solutions exists we still have a rise in the traffic congestion and traffic density is worsening.
There exists no effective method of integrating ride-sharing solutions into transport trip planners.
Shared mobility can be highly criticized:
  New York City study:
    300,000 Cars
    With shared mobility we need 60%
    With AMOD…
      137,500

## Slide 6: Motivation:
The principal trip of passengers in urban zones or in peripheral urban zones.
  2.148 million vs 12,278,210 million
Motivation in integrating both modes of transportation and finding a solution.
Current mobility problems require intelligent solutions.
A research gap
Allowing ride sharing to connect routes with public transit increases the demand.

## Slide 7: Hypothetis:
There is room to improve intermodality between mobility on demand and public transport.
People find difficulty to manage their time during the trip especially when it consistes of taking more than one mode of transportation.
Example 1
Example 2

## Slide 8: Methodology in research:
1. Comprehensive surveys that were published on topics of interest.
2. An overview of application areas of DARPs and routing problems in general.
3. A detailed taxonomy of the problem variants.
4. Identification of potential research gaps.

## Slide 9: Shared Mobility

## Slide 10
A survey on research developments on dial-a-ride problem since 2007.
Proposed solutions:
  One of the proposed solutions are hybrid solutions frameworks for solving the DARP this includes two algorithmic components: dynamic programming (DP) and Large Neighborhood Search (LNS).
  Branch & Cut algorithm is used to find an exact solution using an LP model.
  5000 Taxis and 26,000 bookings.
  Insertion Algorithm.
A natural turn into multimodal trip planning and routing problems.

## Slide 11: Intermodel passenger mobility

## Slide 12
Opportunity for transportation agencies to address the “last mile problem”
The possibility of realizing a seamless integration of ride-sharing and public transit.
Study the transport feeding challenge with autonomous mobility on demand in highly dense cities.
Connecting between routes

## Slide 13: Shared Mobility + Intermodality

## Slide 14
Inter-modality and multimodality exists in literature.
A clear lack of research output in DARP optimization problems when it comes to intermodal trip planning.
Same results in autonomous mobility on demand.

## Slide 15: To conclude:
The research gap exists.
To date, there exist no optimization frameworks that capture optimal coordination policies for MOD systems.
Research assessment: Slow.
A unified method to solve different variants.
No one is responsible if you’re late.

## Slide 16: Problem Definition:
A Dial-a-ride problem.
Pickup location.
Timeslots

## Slide 17: Time Sequence:

## Slide 20: Mathematical Formulation:
Stations Allocation
Driver Allocation
Architecture and flow

## Slide 21: Part I
Minimize:
« n » number of bookings
« m » number of stations
« f » opening cost of station j
« c » travel cost from booking i to station j

## Slide 22: Part II
« B » is the number of shifts available
« N » number of pickups, depots and destinations
« C » cost function w.r.t driver b going from location i (p/d) to location j (p/d)
Minimize:

## Slide 23: Structure & flow:
Population generator
Station assignment problem
Driver assignment and routing problem
Data analysis
Programming Language & solver

## Slide 24: Architecture:

## Slide 25: Results:

## Slide 26
25 Bookings
10 Timeslots
16 Pickup Stations

## Slide 27
13
3

## Slide 28
Average wait time: 24min
Total distance walked: 36.750km
Total Distance travelled by vehicles: 323.96km

## Slide 30: Results & observations:
The data shows that there is a way to make the passengers wait less using darp with time windows in favor of minimizing the wait time.
Comparative studies with real data.
Shared mobility is a non formal feeder to public transport.
Reduce carbon footprint.
Speed of the solver vs timeslots.
Limitations.

## Slide 31: The contribution of this project:
The state of the art & literature review.
Case studies analyzing the potential impact of feeding transport systems.
Ability to identify relevancy.
In the state of the art section I showed the connection in literature between public transport and shared mobility
I showed how can the DAR problem be reformulated to answer to the gap that currently exists
I gained confidence & motivation to continue in this research.
Programming Skills (Julia, Python, Gurobi & CPLEX)

## Slide 32: Next steps:
Create a mathematical formulation for the whole model.
Optimize the whole model and compare results.
Integrate timetables.
Merge real-time booking with prearranged booking.
Include real geographic locations and use real routing data.
Add constraints to the location of pickup stations.
A framework of ride-sharing algorithms to connect all modes of transportation.

## Slide 33: Access to the project:
@aymanmahmoud

## Slide 34
Thank You !